Supplementary Data 1. Real-time reverse transcriptase polymerase chain reaction (rRT-PCR) laboratory procedure

The rRT-PCR assay was performed according to the manufacturer’s instructions. The primer and probe sequences were used according to the previous study. The primer and probe sequences for E gene detection are: 5′- ACAGGTACGTTAATAGTTAATAGCGT-3′ (Forward), 5′- ATATTGCAGCAGTACGCACACA-3′ (Reverse) and 5′- ACACTAGCCATCCTTACTGCGCTTCG-3′ (Probe in 5-FAM/3′-BHQ format) and the primer and probe sequences for the RdRP gene detection are: 5′- GTGARATGGTCATGTGTGGCGG-3′ (Forward), 5′- CARATGTTAAASACACTATTAGCATA-3′ (Reverse), 5′-CAGGTGGAACCTCATCAGGAGATGC-3′ (Probe specific for SARS-CoV-2 in 5-FAM/3′-BHQ format) and 5′-CCAGGTGGWACRTCATCMGGTGATGC-3′ (Pan Sarbeco-probe in 5-FAM/3′-BHQ format). The PCR reaction was performed in a total volume of 20 μL reaction, containing 5 μL of RNA, 11 μL of PCR reaction mixture and 4 μL of primer and probe mixture. Thermal cycling conditions were as follows: 50°C for 30 minutes for reverse transcription, inactivation of the reverse transcriptase at 95°C for 10 minutes, 40 cycles of PCR amplification at 95°C for 15 seconds and 60°C for 1 minute in the CFX96 real-time PCR detection system (Bio-rad, Hercules, CA, USA). For each run, viral template-positive controls and no-template controls were included. Each sample was defined as positive if the Ct values are less than or equal to 35 cycles.

Reference

1. Corman VM, Landt O, Kaiser M, Molenkamp R, Meijer A, Chu DKW, et al. Detection of 2019 novel coronavirus (2019-nCoV) by real-time RT-PCR. Euro Surveill. 2020;25(3).